## Slide 1
Team ID: [Enter ID] Team Name: [Enter Name] Team Leader Name: [Enter Leader] University/Institute/College: [Enter Details] Theme: Hardware / IoT P.S Category: Software/Hardware/Both P.S ID: [Enter PS ID]

## Slide 2
Team Leader: [Name] - [Department] Team Member 2: [Name] - [Department] Team Member 3: [Name] - [Department] Team Member 4: [Name] - [Department]

## Slide 3
Voice-Guard: Standalone IoT Women's Safety Device • Proposed Solution: A discreet, wearable device (ESP32 + SIM800L) that sends instant SOS SMS alerts with location directly to guardians via cellular networks, entirely bypassing the need for a smartphone or Wi-Fi. • How it addresses the problem: In emergencies, unlocking a phone or finding an app is nearly impossible. Voice-Guard provides an immediate 1-button panic response. • Innovation & Uniqueness: 100% Offline operation. Configured securely via a Web-USB app. Includes an Android Guardian App that intercepts the SMS to override silent mode and sound a siren.

## Slide 4
Technologies Used: • Hardware: ESP32 Microcontroller, SIM800L Module, Li-Po Battery, TP4056. • Software: C++ Firmware, Web Serial API (Configurator), React Native/Expo (Android App). Methodology (Flow): 1. Setup: User plugs device into PC -> Web App pairs via USB -> Contacts flashed to NVS memory. 2. Trigger: SOS Button pressed -> ESP32 wakes -> SIM800L dispatches SMS via cell tower. 3. Action: Guardian App receives SMS -> Bypasses silent mode -> Maps live location.

## Slide 5
• Feasibility: Highly feasible. The core components (ESP32 and SIM800L) are inexpensive and mass-produced. Standard 2G/4G networks provide ubiquitous global coverage for SMS. • Potential Challenges & Risks: 1. Cellular dead zones (basements). 2. Battery degradation over time. • Mitigation Strategies: Implemented an ESP32 deep-sleep mode, extending battery life to weeks on a single charge. Added a localized loud buzzer to act as a physical deterrent if SMS fails to send.

## Slide 6
• Potential Impact on Target Audience: Provides immediate peace of mind for women traveling alone, night-shift workers, and students. Dramatically reduces response times during critical incidents. • Benefits of the Solution: 1. Social: Empowers users with a reliable safety net, discouraging predatory behavior. 2. Economic: Designed for affordability (~₹650 per unit in bulk), making life-saving tech accessible across all income demographics. 3. Technological: Bridges the gap between raw hardware and consumer-friendly apps.